## Slide 1: Optical astronomical spectroscopy at the VLT (Part 1)
F. Pepe
Observatoire de Genève

## Slide 2: Course outline
PART 1 - Principles of spectroscopy
  Fundamental parameters
  Overview of spectrometry methods
PART 2 – ‘Modern’ spectrographs
  ‘Simple’ spectroimager
    FORS
  Echelle spectrographs
    UVES
    CRIRES
PART 3 - Spectroscopy on the VLTs
  Multi-Object spectrographs (MOS) and Intergral-Field Units (IFU) and spectro-imagers
    Giraffe
    VIMOS
    Sinfoni
  Future instruments
    X-shooter
    MUSE
    ESPRESSO

## Slide 3: The observables
Propagation of light wave from stable source at infinity:
which is a solution of wave equations if:
cn is the speed of light in a medium with refractive index n = n(k)
Independent observables are:
The distance between two spatial maxima of the light wave in a given medium and at fixed t is called wavelength and results to be:

## Slide 4: The observables
Astronomical spectroscopy aims at measuring:
At optical wavelength n=w/2p is 1015 Hz, thus too fast to be resolved by detectors. The observable becomes the (surface) brightness or specific intensity In or Il:

## Slide 5: The observables
If we integrate the surface brightness over a given source or sky aperture, we get the spectral flux density Fn or Fl at a given light frequency or wavelength:

## Slide 6: Wavelength or frequency?
Frequency (n, w), associated to time-evolution of E-field
Fixed location (detect oscillation amplitude as a function of time)
Need for precise clock (time metric)
Need for time resolution (or other tricks, e.g. heterodyne detection)
Wavelength (l, k), represents light propagation in space
Fixed time (project wave into physical space or spatially separate various spectral components)
Depends on medium ->
Need for precise metrology (space metric) or calibration

## Slide 7: Filter spectrometer
Filter
Telescope
Focal plane
Objective
Detector (single or array)

## Slide 8: Filter spectrometer
Detector records Il for a given filter with transmittance tc, central wavelength lc, and band width Dl
tc, Dl and lc need to be calibrated on standard sources
Appropriate for broad-band spectra
Only one channel per measurement (unless dichroics are used)

## Slide 9: Filter spectrometer
Filter 1
Telescope
Objective
Detector (single or array)
Filter 2
Dichroic

## Slide 10: Fabry-Pérot spectrometer
Telescope
Focal plane
Objective
Detector
Collimator
Fabry-Pérot etalon
Slit

## Slide 11: Fabry-Pérot spectrometer
Similar to filter spectrometer, but spacing can be made tunable
Detector records I(l) as a function of the transmitted wavelength ml=2l, where m is an integer and enumerates the transmitted order.
Only one spectral channel per measurement
Transmittance and wavelength must be calibrated.
Allows high spectral resolution, if the finesse F or the order m is high. In the latter case, a pre-filtering is required to select only one wavelength (order-selection).

## Slide 12: Fabry-Pérot spectrometer
Order-separating filter (e.g. with second FP in 1st order)

## Slide 13: Fabry-Pérot spectrometer
Telescope
Focal plane
Objective
Detector
Collimator
Fabry-Pérot etalon
Slit
Real Fabry-Pérot:
D
f
D

## Slide 14: Example of apearture finesse
Transmitted wavelength is unique only for given angle T
If slit is too wide, the aperture (angle cone) is enlarged and the range of transmitted wavelength increased.
The ‘contrast is the reduced, thus the finesse and the spectral resolution

## Slide 15: General spectrograph layout
Telescope
Focal plane
Objective
Detector
Collimator
Disperser
Slit
Single detector -> monochromator (may be used with movable part to scan over wavelengths
Array detector -> spectrograph with N wavelength channels (N = number of detectors or pixels)

## Slide 16: Dispersers
The disperser separates the wavelengths in angular direction. To avoid angular mixing, the beam is collimated. The disperser is characterized by its angular dispersion:
where b is the deviation angle from the un-dispersed direction

## Slide 17: The prism

## Slide 18: Prism characteristics
Prism example: BK7 (normal glass), t = 50 mm, D = 100 mm
-> High transmittance
-> When used at minimum deviation, no anamorphosis (beam dia. compression or enlargement)
-> Produces ‘low’ dispersion

## Slide 19: Prism characteristics
-> Depends mainly on glass material (internal transmittance)
-> Anti-reflection coatings are needed to avoid reflection losses, especially for large apex angles (and large a). The coating must be optimized for the glass and the used angles.
-> Efficiency can be as high as 99%
-> The dispersion increases towards the blue wavelengths. For Crown glasses (contain Potassium) the ratio of the dispersion between blue and red is lower than for Flint glasses (contain lead, titanium dioxide or zirconium dioxide) .

## Slide 20: Grating spectrograph
Camera
Collimator
Focal ratios defined as
Fi = fi / Di

## Slide 21: The diffraction grating
Generic grating equation from the condition of positive interference between various ‘grooves’:

## Slide 22: Grating characteristics
Typical grating example: m = 1, r = 1000 gr/mm, sina + sinb = 1, cosb=1/2
-> Several orders result for a given wavelength
-> m = 0 for a grating which acts like a mirror -> no dispersion!
-> Orders overlap spatially -> must be filtered or use at m=1
Dispersion typically much higher than for prisms!

## Slide 23: Grism efficiency
Maximum efficiency obtained when specular groove reflection is matches (Blaze condition):

## Slide 24: Order overlaps
0
lU
2lL
2lU
lL
Wavelength in first order marking position on detector in dispersion direction (if dispersion ~linear)
Effective passband
in 1st order
1st order
blaze profile
Passband
in zero
order
m=1
m=2
m=0
2nd order
blaze profile
Intensity
Passband
in 2nd order
First and second
orders overlap!
Don't forget higher orders!
0
lL
lU
1st order
(2nd order)
lC
Zero order
matters for MOS

## Slide 25: Resolving power and resolution
Camera
Collimator
Focal ratios defined as
Fi = fi / Di

## Slide 26: Resolving power and resolution
The objective translates angles into positions on the detector. Each position (pixel) of the detector ‘sees’ a given angle of the parallel (collimated) beam
The collimated beam is never perfectly parallel, because either of the limited diameter of the beam, which produces diffraction df = 1.22 l/D1, or because of the finite slit, which produces and angular divergence dQ = s/f1.
The angular divergence is translated into a distance dl = f2 dQ or dl = f2 df on the CCD. This means that over this distances the wavelengths are mixed (cannot be separated angularly.

## Slide 27: Resolving power and resolution
Resolving power is the maximum spectral resolution which can be reached if the slit s = 0 and the angular divergence is limited by diffraction arising from the limited beam diameter. For a given Dispersion D we get the resolving power:
Spectral resolution is the effective spectral resolution which is finally reached when assuming a finite slit s. For a given Dispersion D we get the spectral resolution:

## Slide 28: Conservation of the ‘étendue’
The étendue is defined as E=A x O, where A is the area of the beam at a given optical surface and O is the solid angle under which the beam passes through the surface.
When following the optical path of the beam through an optical system, E is constant, in particular, it cannot be reduced
For a telescope, E is the product of the primary mirror surface and the two-dimensional field (in sterad) transmitted by the optical system. Normally, the transmitted field is defines a slit width. When entering spectrograph, the slit x beam aperture at the slit is equal to the etendue E of the telescope. This implies that at fixed spectral resolution, the slit width and the beam diameter cannot be chosen independently, since dQ depends on both.

## Slide 29: Other dispersers
Grisms
VPHG
Echelle grating

## Slide 30: Grisms
Transmission grating attached to prism
Allows in-line optical train:
  simpler to engineer
  quasi-Littrow configuration - no variable anamorphism
Inefficient for r > 600/mm due to groove shadowing and other effects

## Slide 31: Grism equations
Modified grating equation:
Undeviated condition:
  n'= 1, b = -a = f
Blaze condition: q = 0  lB = lU
Resolving power
(same procedure as for grating)
q = phase difference from centre of one ruling to its edge

## Slide 32: Volume Phase Holographic gratings
So far we have considered surface relief gratings
An alternative is VPH in which refractive index varies harmonically throughout the body of the grating:
Don't confuse with 'holographic' gratings (SR)
Advantages:
  Higher peak efficiency than SR
  Possibility of very large size with high r
  Blaze condition can be altered (tuned)
  Encapsulation in flat glass makes more robust
Disadvantages
  Tuning of blaze requires bendable spectrograph!
  Issues of wavefront errors and cryogenic use

## Slide 33: VPH configurations
Fringes = planes of constant n
Body of grating made from Dichromated Gelatine (DCG) which permanently adopts fringe pattern generated holographically
Fringe orientation allows operation in transmission or reflection

## Slide 34: VPH equations
Modified grating equation:
Blaze condition:
= Bragg diffraction
Resolving power:
Tune blaze condition by tilting grating (a)
Collimator-camera angle must also change by 2a  mechanical complexity

## Slide 35: VPH efficiency
Kogelnik's analysis when:
Bragg condition when:
Bragg envelopes (efficiency FWHM):
  in wavelength:
  in angle:
Broad blaze requires
  thin DCG
  large index amplitude
Superblaze
Barden et al. PASP 112, 809 (2000)

## Slide 36: Other dispersers
Grisms
VPHG
Echelle grating …